Network Lab 3
Abhiraj Tiwari (180905422)
# Question 1

# Question 2
There are 256 addresses in this block. the first address is 14.24.74.0/24; The last address is 14.24.74.255/24.
The number of addresses in the largest subblock ,which requires 120 addresses, is not power of 2, we allocate 128 addresses .The subnet mask for this subnet can be found as 32 -log2128 =25. The first address in this block is 14.24.74.0/25 ; the last address is 14.24.74.127/25.

The number of addresses in the second largest subblock , which requires 60 addresses , is not a power of 2 either, we allocate 64 addresses .The subnet mask for this subnet can be found as 32 - log264 = 26.The first address in this block is 14.24.74.128/26;The last address is 14.24.74.191/26

The number of addresses in the smallest subblock ,which requires 10 addresses, is not a power of 2 either.we allocate 16 addresses.The subnet mask for this subnet can be found as 32-log216 = 28. The first address in this block is 14.24.74.192/28; The last address is 14.24.74.207/28
# Question 3

# Question 4

##### Cloud 1
R1(config)#interface fastEthernet 0/0
R1(config-if)#no shut
R1(config-if)#ip address
R1(config-if)#ip address 14.24.74.0 255.255.255.128
R1(config-if)#exit
R1(config)#ip dhcp pool cloud3
R1(dhcp-config)#default-router 14.24.74.0
R1(dhcp-config)#network 14.24.74.0 255.255.255.128
R1(dhcp-config)#exit
##### Cloud 2
R1(config)#interface fastEthernet 0/1
R1(config-if)#no shut
R1(config-if)#ip address
R1(config-if)#ip address 14.24.74.129 255.255.255.192
R1(config-if)#exit
R1(config)#ip dhcp pool cloud3
R1(dhcp-config)#default-router 14.24.74.129
R1(dhcp-config)#network 14.24.74.129 255.255.255.192
R1(dhcp-config)#exit
##### Cloud 3
R1(config)#interface fastEthernet 1/0
R1(config-if)#no shut
R1(config-if)#ip address
R1(config-if)#ip address 14.24.74.192 255.255.255.240
R1(config-if)#ip address 14.24.74.193 255.255.255.240
R1(config-if)#exit
R1(config)#ip dhcp pool cloud3
R1(dhcp-config)#default-router 14.24.74.193
R1(dhcp-config)#network 14.24.74.193 255.255.255.240
R1(dhcp-config)#exit